## Slide 1: Concentration Units
Molarity
Formality:
Normality
What is the molarity of a 6N H2SO4 solution?
How do you make 100mL of a 4N H2SO4 solution from conc. H2SO4?

## Slide 2: Sampling
Difficult in real world
So2 = sm2 + ss2
Where:
so2 = overall variance
s = standard deviation
sm2 = variance of analytical method
ss2 = variance of sampling

## Slide 3: Cork
l___l___l___l___l___l___l___l___l___l___l
0 10 20 30 40 50 60 70 80 90 100
Rubber
l___l___l___l___l___l___l___l___l___l___l
0 10 20 30 40 50 60 70 80 90 100

## Slide 4: Sampling alone can introduce significant error
Sampling error will be significant whenever the # of defining units becomes too few
Std. deviation associated with sampling can be defined as:
sn = npq
n = # of particles taken
p = probability of drawing A = nA/(nA + nB)
q = probability of drawing B = nB/(nA + nB)

## Slide 5: Grab and Composite Samples
Grab: Individual sample collected at a particular time and place – example
Limitations:
Composite: Mixture of grab samples taken over a period of time – example
Limitations:

## Slide 6: To composite or not composite

## Slide 7: Compositing Demo
Analysis # | Mixed | Core
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
Mean |  | 
Std. dev. |  | 

## Slide 8: How do you know when you have taken enough samples?

## Slide 9: Types of Sampling Schemes
Random: no operator bias, least uncertainty, largest # of samples
Stratified: judgemental, requires least # of samples, used most often, based on prior knowledge, most uncertainty
Systematic: 1st sample is randomly chosen, after that taken at fixed time & space intervals Lake diagram

## Slide 10: What is the best sampling scheme for my project?
Consider
  Costs
  Use of data
  Heterogenity of system
  Pollutant mobility
  Most projects will require more than one sampling strategy examples

## Slide 11: Sampling strategy?

## Slide 12: Sampling strategy?

## Slide 13: Quality control
Contamination
Preservation and storage
Duplicates: 10% duplicate amount necessary
Split samples
Reagent blank
Method blank
Matrix spike

## Slide 14: Quality Control
Blind field duplicates
Field QC checks
Field blanks
Trip blanks

## Slide 15: Field records documentation requirements
Name of sample collector
Date and time of sampling
Field conditions:
Sample type
Label with requested analytical parameters and preservation technique
Chain of custody