## Slide 1: Primary Standards
Is a highly purified compound that serves as a reference material in all volumetric and titrimetric methods. It must be:
  1) Highly pure, established methods for confirming purity should be available.
  2) Stable toward air
  3) Absence of hydrates of water so that the composition of the solid does not change with variations in relative humidity

## Slide 2: Primary standards continued
4) Readily available at reasonable cost.
5) Reasonably soluble in titration medium.
6) Reasonably large molar mass so that the relative error associated with weighing the standard is minimized.
Examples?
KHP, AgNO3

## Slide 3: Secondary standards
Hard to find primary standards therefore secondary standards are often used.
Secondary standard is a compound whose purity has been established by chemical analysis and serves as a reference material for titrimetric methods of analysis.
Examples?
NaOH, EDTA

## Slide 4: External standards
A standard that is analyzed separately from the replicate unknowns being tested.
Example?
Phosphorus

## Slide 5: External Standard example
The amount of phosphorus in an effluent sample from the Winona wastewater treatment plant was diluted in half and then analyzed for its phosphorus content by an absorbance method. The absorbance measured was 0.252. A calibration curve was run at the following concentrations with the corresponding absorbances: What is the concentration of phosphorus in the original sample?
Concentration (ug/L) | Absorbance
0 | 0.000
.25 | 0.078
.5 | 0.191
1.0 | 0.399

## Slide 6: Internal Standards
Internal standards are analyzed at the same time as the unknown analytes
Involves:
1) Adding a single spike to each replicate and the blank.
2) Internal standard must be sufficiently different from the sample such that while it is detected in the same experiment, it does not interfere with the assay

## Slide 7: Internal standards continued
This can be challenging!
3) Used for quantitation to check recovery.

## Slide 8: Internal Standard Example
In my research lab, in the past, I have been trying to determine the amount of sulfanamide in 500mL of water by high performance liquid chromatography (HPLC). In order to meet the detection limit of the instrument I must pre-concentrate the water on a solid phase extraction cartridge and extract it off in = 2mL of methanol. The methanol extract is then analyzed on the HPLC. In order to quantitate sulfanamide, the internal standard sulfanilic acid (SA) is added to the extract. A standard sulfanamide and SA chromatogram gave area counts of 32641890 and 27644018 respectively for sulfanamide and SA amounts of 0.507 and 0.511mg respectively. A chromatogram containing an unknown amount of sulfanamide and 0.511mg of SA resulted in peaks with areas of 50711602 and 43651897 for sulfanamide and SA respectively. What was the concentration of sulfanamide (mg/L) in the original 500mL water sample?