## Slide 1: Spectroscopy
Utilizes the various regions of the electromagnetic spectrum to detect signal

## Slide 2: Different regions
g rays result from nuclear transitions Scintillation counting, g ray emission, radioactive assays, and DNA fingerprinting
X-rays result from inner e- transitions x-ray powder diffraction
UV results from changes in bonding e- UV spectroscopy
Visible also from bonding e- transitions visible spectroscopy
Visible also from bonding e- transitions visible spectroscopy

## Slide 3: Different Regions
Microwave results from rotation of molecules microwave absorption and e- spin resonance
Radio results from spin of nuclei in magnetic field NMR
IR results from vibration and rotation of molecules IR and Raman spectroscopy

## Slide 4
Frequency: # of oscillations to the field per second
Wavelength: Distance between any 2 equal points on wave
Wavenumber: 1/l = n

## Slide 5
Transmittance:
  T = P/Po
  Where: Po = initial power of beam
  P = power of beam passing through sample
  %T = P/Po x 100
  A = -logT
A = ebc
The thicker the glass the darker the brew, the less the light that shines through