## Slide 1: NMR Theory
From physics we know that a spinning charge has an associated magnetic field.
All nuclei have positive charge.
Some nuclei have “spin” and are “NMR active”. These spinning nuclei are, in essence, “nuclear magnets” that will align in the presence of a magnetic field.
  NMR active nuclei: 1H, 13C, 19F, 31P, 2H
  NMR inactive nuclei: 12C, 16O

## Slide 2: NMR Theory
There are 2 variables in NMR: the applied magnetic field (B0) and the frequency ( ) of radiation required for resonance, measured in MHz.

## Slide 3: Effect of B0 on resonance frequency
NMR spectrometers are designated according to the frequency required to make 1H nuclei (protons) resonate. The modern standard is 300 MHz. Early instruments operated at 60 MHz. Top of the line research instruments go as high as 1000 MHz. Stronger magnets are being actively pursued.

## Slide 4: Schematic of an NMR

## Slide 5
This is a nice NMR.

## Slide 6: Resonance Frequency
Different nuclei resonate at greatly different ν : on a 300 MHz instrument (1H = 300 MHz) 13C resonates at 75 MHz.
The same type of nucleus also absorbs at slightly different ν, depending on its chemical environment.
Exact frequency of resonance = “chemical shift”
The strength of the magnetic field actually felt by a nucleus (Beff) determines its resonance frequency.
  Electron clouds shield the nucleus from the magnet
  Circulation of electrons in π orbitals can generate local magnetic fields that influence Beff
Modern NMR spectrometers use a constant magnetic field strength B0, and pulse a broad range of frequencies to bring about the resonance of all nuclei at the same time.

## Slide 7: Example C-13 Spectrum

## Slide 8: Chemical Shift
Peaks on NMR spectrum = “resonances “.
Chemical shift is measured in ppm
  ppm = ν in Hz relative to ref peak/instrument ν in MHz.
Reference peak = 0 ppm = (CH)4Si = tetramethylsilane (TMS). TMS is an inert compound that gives a single peak at lower frequency than most typical NMR peaks.
Protons absorb between 0-10 ppm. C-13 nuclei absorb between 0-250 ppm.

## Slide 9: Electronic Shielding
More electron density = more shielding
Less electron density = less shielding

## Slide 10: Shielding in Spectrum

## Slide 11: Predicting the Number of C-13 Peaks
The most important aspect in interpreting a C-13 NMR spectrum is checking the number of resonances displayed against the number of resonances theoretically expected from the structure.
Nuclei that have the exact same chemical environment (because of symmetry in the molecule) are said to be chemically equivalent and give only one resonance.
(Rarely two or more nuclei may give a single peak even though they do not have the exact same chemical environment. In this case the nuclei are said to be coincidentally equivalent. In other words, the resonances overlap. This is more common in very large molecules and less common at high magnetic field strengths.)