## Slide 1: Chapter 3 Mechanical Properties of Materials

## Slide 2: Obtaining Stress and Strain Values from Testing
The nominal or engineering stress can be determined by dividing the applied load, P (measured by the load cell on the test frame), by the original cross-sectional area, Ao, of the specimen
The nominal or engineering strain can be determined either by using a strain gauge or an extensometer
A strain gauge or extensometer determines strain by measuring a specimen's change in length, δ, and dividing this quantity by a set gauge length, Lo

## Slide 3: Conventional Stress-Strain Diagram
σ - ε diagram for a steel (upper figure is not drawn to scale, lower figure is drawn to scale)
Proportional limit (σpl): stress is proportional to the strain, material behaves linearly elastic
Elastic limit: upon load removal, specimen still returns back to its original shape
Yield stress or yield point (σY): deformation that occurs is plastic deformation, after reaching (σY) specimen continues to elongate without any increase in load
True σ - ε curve uses the actual cross-sectional area and length of the specimen at the instant the load is measured

## Slide 4: Stress-Strain Behavior of Ductile and Brittle Materials
Ductile Materials
  Experience large stains before fracture
  Percent elongation ((Lf – Lo)/Lo * (100%))
  Percent reduction in area (within the region of necking, (Ao – Af)/Ao * (100%))
  Some materials may not exhibit a well-defined yield point, standard practice to define a yield strength using a graphical procedure known as the offset method (often a 0.2% strain is the offset used)
Brittle Materials
  Exhibit little or no yielding before failure
  Compared with behavior in tension, brittle materials typically exhibit much higher resistance to axial compression
Materials can exhibit both ductile and brittle behavior (i.e. steel has brittle behavior when it contains a high carbon content and is ductile when the carbon content is reduced)

## Slide 5: Hooke's Law
For most engineering materials a linear relationship exists between stress and strain within the elastic region
In equation form this relationship is known as Hooke's Law
  E represents the constant of proportionality and is called the modulus of elasticity or Young's modulus
  Represents the equation of the initial straight-lined portion of the σ - ε diagram up to the proportional limit and E is the slope of this line
  E is a (inherent) mechanical property that reflects the "stiffness" of a material
  E will have units of stress such as Pa or psi
If a material fails to exhibit linear-elastic behavior or if the stress in the material exceeds the proportional limit, the σ - ε diagram ceases to be a straight line and Hooke's Law is no longer valid

## Slide 6: Permanent Set
If a specimen of ductile material is loaded into the plastic region and then unloaded, elastic strain is recovered as the material returns to its equilibrium state
The plastic strain remains and the material is subjected to a permanent set

## Slide 7: Strain Hardening
If a load is reapplied following a loading/unloading cycle, the material will again be displaced (moving along approximately the same slope as the initial loading cycle) until yielding occurs at or near the stress level reached previously
The σ - ε diagram now has a higher yield point as a result of strain hardening
The material now has a greater elastic region, yet less ductility (a smaller plastic region)
In actuality some heat or energy may be lost as the specimen is unloaded and then reloaded resulting in slight curvature in the path followed
The area in between these curved lines represents lost energy and is termed mechanical hysteresis

## Slide 8: Strain Energy
As a material is deformed by an external loading, it tends to store energy internally throughout its volume
Since the energy is related to the strains in the material it is known as strain energy
The external work done to the material (the product of the force and displacement in the direction of the force) is equivalent to the internal work or strain energy
Strain-energy density is the strain energy per unit of volume

## Slide 9: Modulus of Resilience
Modulus of resilience, μr, is equivalent to the triangular area under the proportional limit
μr represents the largest amount of strain energy per unit volume a material can absorb without causing any permanent damage to the material

## Slide 10: Modulus of Toughness
Modulus of toughness, μt, is the entire area under the σ - ε diagram
μt represents the maximum amount of strain energy per unit volume a material can absorb up to fracture
Materials with a high μt will distort greatly due to an overloading, materials with a low μt may suddenly fracture without warning of an approaching failure
Problems pg 102

## Slide 11: Poisson's Ratio
When a load P is applied to a bar, it changes the bar's length by an amount δ and it's radius (or other perpendicular dimension) by an amount δ'
Within the elastic range the ratio of these strains is a constant
  Poisson's ratio (ν or nu),
  Negative sign is used since longitudinal elongation (positive strain) causes lateral contraction (negative strain), and vice versa (and Poisson's ratio is a positive value)
  Poisson's ratio is dimensionless and typically has a value between 1/4 and 1/3 (0<=ν<= 0.5)

## Slide 12: Shear Stress-Strain Diagram
Hooke's law for shear
G is called the shear modulus of elasticity or the modulus of rigidity (same units as E)
The three material constants E, ν, and G are related by the following equation (for isotropic materials)
Problems pg 113