## Slide 1: Environmental Regulation - Defining the ”Alphabet Soup"

## Slide 2: Why?
EPA enforcement actions, https://echo.epa.gov/facilities/enforcement-case-search
MPCA enforcement actions, https://www.pca.state.mn.us/regulations/enforcement

## Slide 3: RCRA (Resource Conservation and Recovery Act of 1976)
essence of national policy on hazardous waste
most all hazardous waste mgmt activities are affected by RCRA regulations
goals:
  (1) describe the wastes and the participants affected by RCRA
  (2) track location of all hazardous wastes, systematically, from point of generation to ultimate disposal
  (3) to promote waste mgmt practices that ensure the protection of human health and the environment

## Slide 4: RCRA's Basic Set-up (as defined in the CFRs)
waste determination (hazardous or nonhazardous)
EPA identification numbers for each generator (as well as transporters and TSDFs)
manifesting (uniform shipping document required by the EPA and established as a tracking mechanism)
packaging, labeling, marking, and placarding prior to transport
record keeping and reporting

## Slide 5: Additional Regulation Resulting from RCRA
RCRA imposes stringent technical rqmts on TSDFs (i.e. landfills, surface impoundments, and other waste mgmt units must be designed and operated in order to prevent migration of contaminants into the environment)
land bans
  move generators and waste mgmt companies away from land disposal → waste reduction, recycling and reuse (the three R's)
  rules to restrict land disposal of "scheduled" wastes (over 400 listed wastes)
HSWA (Hazardous and Solid Waste Amendments, 1984)
  remedy source of confusion (broad statutory language) and regulatory loopholes of RCRA
  include regulations to:
    control leaking of USTs
    better manage waste of small-quantity generators
    phase out land disposal of untreated hazardous waste
    identify additional hazardous wastes
    set specific controls on the burning and blending of hazardous waste as fuels
EPA link

## Slide 6: TSCA (Toxic Substances Control Act, enacted 1976)
designed to screen out the use of any existing, imported, or new chemicals that present a hazard to human health or the environment (i.e. PCBs, asbestos)
anyone who manufactures or imports a chemical that does not appear on the TSCA chemical list (contains 83,000 chemicals) must make a "premanufacture notification" (PMN)
PMN must include:
  detailed chemical description of the substance, the process that forms it, its by-products, its use, and typical amounts used
  facilities where it is used, number of workers involved with the chemical and related occupational exposure info, and environmental emissions info
  submission of any existing environmental, health and safety data
  determination of disposal hazards and recommendation of waste-handling procedures
  EPA has 90 days either to approve or request more info
EPA link

## Slide 7: CERCLA (Comprehensive Environmental Response, Compensation, and Liability Act of 1980)
Superfund (original focus on closed hazardous-waste sites)
EPA link
SARA (Superfund Amendments and Reauthorization Act, 1986)
  reauthorized CERCLA to continue cleanup activities around the country
  SARA Title III or EPCRA (Emergency Planning and Community Right to Know Act) - mandates comprehensive chemical reporting and community participation rqmts (EPA link)

## Slide 8: SARA Title III (EPCRA) Section 311
applies to companies that maintain SDSs for their workers and who have present at any time during the year 10,000 lbs or more of OSHA chemicals or 500 lbs or more of "extremely hazardous substances" or the Threshold Planning Quantity (TPQ) for those chemicals, whichever is less
  companies must submit SDSs or list of chemicals to State Emergency Response Commission (SERC), Local Emergency Planning Committee (LEPC) and the local fire dept
  one time reporting rqmt

## Slide 9: SARA Title III (EPCRA) Section 312
companies that must comply with Section 311 must also submit inventory (Tier I or Tier II forms) info
inventory info includes:
  facility info
  emergency contacts
  CAS numbers for reported chemicals
  chemical names
  hazard types
  minimum daily amts
  avg daily amts
  number of days on site
  storage location

## Slide 10: SARA Title III (EPCRA) Section 313
manufacturers that have 10 or more employees and manufacture or process over 25,000 lbs of specified chemicals (list contains over 600 chemicals and 20 chemical categories) must file (annually) a Toxic Release Inventory (TRI) with EPA and the states
Pollution Prevention Act of 1990 (which amended EPCRA) also requires the TRI to include info on company's efforts to reduce waste, recycle and to recover energy from its processes

## Slide 11: CWA (Clean Water Act, enacted 1972) (last amended as the Water Quality Act of 1987)
regulates discharges of municipal wastewater treatment plants and industrial wastewater treatment operations
NPDES (National Pollutant Discharge Elimination System)
  "effluent standards" established for numerous pollutants (about 100 chemicals)
  standards are enforced by the issuance and monitoring of NPDES permits by EPA of the states
also regulates discharge of toxics-laden wastewater in publicly owned treatment works (POTW), originating with industrial discharges into sewers → EPA has established "pretreatment standards" for certain wastewater pollutants
EPA link

## Slide 12: CAA (Clean Air Act, enacted 1955) (amended 1963,'67,'70,'77, and '90)
imposes restrictions on air pollutants from both stationary sources (factories, utilities) and mobile sources (automobiles, aircraft)
NAAQS (National Ambient Air Quality Standards) restrict the levels of six "criteria" pollutants: sulfur oxides, carbon monoxide, nitrogen oxides, ozone (including volatile organic compounds, VOCs), particulate matter and lead
NESHAP (National Emission Standards for Hazardous Air Pollutants) regulates hazardous substances, or air toxics
EPA link

## Slide 13: MACT standards for the composites industry
in 1990 amendment of CAA, Congress told EPA to issue emission control regulations for industries emitting one or more of the listed HAPs
styrene, and in lesser amounts methyl methacrylate and methylene chloride are HAPs emitted by composites manufacturers
major sources of emissions are to adopt what EPA determines is the maximum achievable control technology (MACT)
  for existing sources MACT must be set at a level of control at least as stringent as that achieved by the average of the best performing 12% of sources in that industry
  for new sources MACT must be as stringent a level of control achieved by the single best performing source
the NESHAP (MACT Standard) for the Reinforced Plastics/Composites source category
  EPA and the composites industry began work on MACT for composites in 1993
  the proposed MACT Standard was published in the Federal Register on August 2, 2001
  the final MACT Standard was signed February 28, 2003 by EPA Administrator Christine Whitman
  in open molding operations, the use of low styrene content resins and gel coats, vapor suppressants, and non-atomizing application equipment should lead to compliance
  https://www.epa.gov/stationary-sources-air-pollution/national-emission-standards-hazardous-air-pollutants-reinforced-1