## Slide 1: Health and Safety Issues in Composites Manufacturing

## Slide 2: Review Safety Data Sheet, SDS (previously Material Safety Data Sheet, MSDS)
Interplastic Corp Polyester Resin (COR60-239-034)
  Tech Data Sheet
  SDS
West System Epoxy Resin System
  105 Epoxy SDS
  206 Slow Hardener SDS
OSHA pictograms

## Slide 3: Health Information Terminology
toxicity
  the inherent harmful effect of a chemical
  all chemicals, no matter how "safe" one thinks they may be, are toxic
  it is an unchangeable property of the chemical as is its color, odor or other physical properties
hazard
  takes into account not only this inherent toxicity, but also exposure to the chemical
  without exposure even most toxic chemical presents no hazard
  likewise, if one is exposed to a large amount of a chemical with relatively low toxicity, the resultant hazard may be great

## Slide 4: Acute Toxicity
harmful effect after a single or short-term exposure
most common measure of acute toxicity is LD50 (median lethal dose)
  mg of chemical/kg of body weight
  would be expected to kill 50% of a group of experimental animals
parallel measure of acute inhalation toxicity is given by the LC50 (median lethal concentration)
  airborne concentration in mg chemical per cubic meter of air, or parts per million (ppm) in the air (for conversions calculations see examples)
  normally determined in rats using a 4-hour exposure period
  reported as the LC50 with the time specified
depending on the degree and reversibility of damage at the point of exposure, substances are classified as non-irritants, irritants or corrosives
  irritation
    localized reaction resulting from either a single or multiple exposure to a physical or chemical entity at the same site
    characterized by the presence of redness and swelling and may or may not result in cell death
  corrosives
    will cause irreversible tissue destruction

## Slide 5: Chronic Toxicity
characterized by the adverse health effects in an animal or person which have been caused by
  exposure to a substance over a significant portion of that animal's or person's life
  long-term effects resulting from a single or a few doses
intent of chronic toxicity testing in animals is to define a specific dose or exposure level that will produce a measurable, long-term toxic effect in a target organ (lungs, liver, kidney, etc.)
properly designed chronic toxicity study should provide a "non-observable-effect level" (NOEL)
carcinogenicity
  ability of a substance to cause tumors (cancers) in the body
  experimental time 2-7 years, 2+ years to evaluate data
mutagenicity
  current thinking - many types of cancers have their origins in genetic changes (mutations) that occur in the body’s cells
  ability of substance to cause changes in the genetic material of cells
  alternate short-term test
  not an absolute correlation between mutagenicity and carcinogenicity

## Slide 6: Sensitization
an allergic reaction to a substance that develops upon repeated exposure
causes skin rashes in the case of dermal sensitization, or an asthmatic-type reaction in cases of respiratory sensitization
the extent of the reaction does not necessarily bear a relationship to the degree of exposure
persons sensitized to a certain substance can react strongly to trace amounts of that material
cross sensitization - person who is sensitized to one chemical substance may react to other similar materials

## Slide 7: Exposure Limits – American Conference of Governmental Industrial Hygienists (ACGIH) Threshold Limit Values (TLVs)
airborne concentrations of substances to which nearly all workers may be repeatedly exposed day after day without adverse effect
based on industrial experience and from experimental human and animal studies and a combination of the three
ACGIH (American Conference of Governmental Industrial Hygienists) determines threshold limit values (TLVs) for hazardous substances and physical agents
in a web browser search, “ACGIH TLV for “chemical name“

## Slide 8: Three categories of TLVs established by (ACGIH):
Threshold Limit Value - Time Weighted Average (TLV-TWA): time weighted average for a normal 8-hour workday and a 40-hour work week to which nearly all workers may be exposed without adverse effect
Threshold Limit Value - Short Term Exposure Limit (TLV-STEL): concentration to which workers can be exposed continuously for a short period of time (15 min) without suffering from irritation, chronic or irreversible tissue damage or narcosis (sleepiness), provided the daily TLV-TWA is not exceeded
Threshold Limit Value - Ceiling (TLV-C): the concentration that should not be exceeded during any part of the day

## Slide 9: NIOSH (National Institute for Occupational Safety and Health)
has statutory responsibility for recommending exposure levels that are protective to workers
has identified Recommended Exposure Levels (RELs) for 677 hazardous substances: http://www.cdc.gov/niosh/npg/npg.html

## Slide 10: Exposure Limits - Permissible Exposure Limits (PELs)
issued by the Occupational Health and Safety Administration (OSHA) in 1971
legally binding airborne exposure limits
  Federal
    Jurisdiction
    PELs: 1910.1000 Table Z-1, Table Z-2
  State of MN
largely based on TLVs stemming from research conducted in the 1950’s and 1960’s
  In 1989, OSHA published a final rule for general industry, revising 212 existing exposure limits and establishing 164 new ones
  In 1992, 11th Circuit Court of Appeals vacated the new PELs forcing OSHA to return to the original 1971 limits (the Court ruled that OSHA did not sufficiently demonstrate the new PELs were necessary or that they were feasible)

## Slide 11: Styrene
Since the 1980s, in fact, a variety of state, national and international organizations have assessed the health effects of styrene and deemed it not harmful to humans if managed using the accepted guidelines. However, in 2004, the U.S. National Toxicology Program (NTP), under the U.S. Department of Health and Human Services (HHS), received a recommendation from an unidentified private individual to assess the health effects of styrene. The resulting decision, in June 2011, was to list styrene in the 12th Report on Carcinogens (RoC), officially labeling it as “reasonably anticipated to be a human carcinogen.” Chemical and composites industry trade associations responded swiftly, petitioning the Obama Administration and HHS Secretary Kathleen Sebelius to delist styrene.
Although the NTP lacks direct regulatory authority — that is, the listing does not preclude styrene’s use, nor does it necessarily lead to greater restrictions in terms of its use — the RoC is a nationally recognized, often-referenced document that insurance companies use to justify either increased rates or termination of coverage. For composites manufacturers that use UPR, therefore, the immediate effects are financial. (ref: Composites Technology, Feb 2012)

## Slide 12: Industrial Hygiene in a Composites Manufacturing Company
industrial hygiene - recognition, evaluation, and control of workplace conditions which may cause sickness, impaired health, or significant discomfort among employees
see OSHA Technical Manual (Section III: Chapter 1, Polymer Matrix Materials: Advanced Composites)
typical concerns
  residual monomers of hazardous materials may be released during processing - airborne accumulation of these monomers in the workplace must be minimized
  vapors from cutting agents, solvents and hardeners must be controlled
  cutting, grinding and shaping of cured resins may produce particulates that can contact skin or be inhaled
routes of exposure
  skin and eye (dermal and ocular) contact
  inhalation
  ingestion

## Slide 13: Company Requirements
OSHA Hazard Communication Standard (HCS or Right to Know)
  written plan
  labels and warnings (OSHA pictograms)
  training
  SDSs
emergency preparedness
  fire and explosion emergencies
  medical emergencies
safety procedures
  procedures established and implemented for addressing potentially hazardous operations (i.e. exotherms)
isolation of operations (i.e. paint booth for gel coat application, painting)
housekeeping practices (i.e. vacuum dust do not blow it off work surface)
personal protective equipment (i.e. eye protection, gloves, respirators, ...)
personal hygiene

## Slide 14: Example
Oh my poor friend, he walked into his teenager’s bedroom and accidentally kicked over an open bottle of nail polish remover that was left on the floor (the room is approximately 10' by 12' with a ceiling height of 8'). By the time it was cleaned up about 1.25 cu ft of vapor from the spilled nail polish remover had accumulated in the room. He cracked the window a little, left the bedroom door open, and went down the hall to his bedroom. Upon waking up in the morning (8 hours later) the vapor was barely noticeable (estimated to be around 0.1 cu ft). Knowing nail polish remover is just acetone by another name, my friend was concerned that his child may have been exposed to unhealthy levels of acetone. Assuming a constant rate of decline in the acetone content in the air through the night, was the acetone concentration a hazard? If the exposure had been occupational, would PELs have been exceeded? What about if they lived in Wisconsin?