## Slide 1: Process Improvement (Lean Concepts)

## Slide 2: Origins of Lean
Lean concepts evolved from the JIT philosophy pioneered in Japan by Toyota and embodied in their Toyota Production System
The emphasis of JIT is the elimination of waste throughout the supply chain
In the 1990's companies adopted the term lean in place of JIT

## Slide 3: The Basis of Lean Thinking
Lean means producing
  What is needed
  When it is needed
  With the minimum amount of materials, equipment, labor, and space
Producing what is required, when it is required, but with minimal investment
The goal of an enterprise adopting lean
  Make each process as efficient and effective as possible
  Connecting those processes in a stream or continuous chain that is focused on flow and maximizing customer value

## Slide 4: Flow
Flow is defined as continuous movement of products and information through a value stream
The goal of a lean enterprise is to minimize idle time in the value stream (idle time equates to inefficiency and waste)
Winona Sandwich Company example
  Daily special
  Custom order
  Example parameters
Notes: 1 click = 10 sec, yell left, right, both
10 people, two fists (sandwiches)
Cut bread – 10 sec (open fist)
Add meat – 10 sec (add stir stick)
Add toppings – 20 sec (add penny)
Add condiments – 20 sec (add paperclip)
Packaging – 10 sec (close fist)
Total processing time to make a sandwich: 70 sec
How long before first sandwich complete:
  20 x 10 sec = 200 sec
  20 x 10 = 200
  20 x 20 = 400
  20 x 20 = 400
  1 x 10 = 10
  Total = 1210 sec = 20.17 min
  % of time in process with nothing done to it = (1,210 sec-70 sec)/1,210 sec = 94.2%

## Slide 5: Winona Sandwich Company Daily Special
How long before first sandwich ready?
Majority of time is idle time - no work is being performed on a sandwich
Batch process
  Push system
    Completes a predetermined quantity of work from an established work queue or forecast
    Typically, the work queue or forecast is offset to the actual customer demand to allow time for production and delivery
  High inventory
  High degree of risk
  Yet a great convenience for customers in a hurry
No flow

## Slide 6: Single-piece Flow Process
Winona Sandwich Company Custom order
Single-piece flow process
  Process of creating a sandwich is triggered only when a customer order initiates the process
  Pull System
    Completes a quantity of work that is directly linked to customer demand
    Materials are staged at the point of consumption
    As materials are consumed, signals (kanban) are sent to previous steps in the process to pull forward sufficient materials to replenish only those that have been consumed
Total flow
Ultimately selection of the model to be implemented should be dictated by marketplace demands with the goal of maximizing customer value

## Slide 7: Customer Value
Customer value refers to specific activities that add value to the products and services customers buy
Determination of what is value-added is made from the customer’s perspective
Under lean philosophy for an activity to be value-added it must meet the following three criteria:
  (1) The customer must be willing to pay for the activity
  (2) The part or the object must change (movement?, inspection?)
  (3) It must be done right the first time
Non-value-added activity → waste
Viewing a process in the context of what is truly value-added, a different perspective will emerge for the opportunities for improvement

## Slide 8: Waste
A key tenet under the philosophy of lean and continuous improvement is to minimize non-value-added tasks and eliminate the sources of waste
Seven sources of waste, DOTWIMP (ref: Fiore, Clifford)
Types of Waste | Factory Waste Example
Defects | - Part failing functional test - Part feature violating drawing dimensions
Over-production | - Machining parts with no usage requirement
Transportation | - Moving parts from one machine to another
Waiting | - Partially machined parts on the shop floor queued for the next operation
Inventory | - Completed parts that have not been purchased
Motion | - Extra process steps
Processing | - Part inspection

## Slide 9: Required Waste vs Pure Waste
Waste can be further classified as required waste and pure waste
Required waste represents activities that do not meet the three criteria for a value-added task but are still necessary to support the creation of a product
Activities may be mandated by the customer and/or government regulation (i.e. inspections/tests)
The most obvious examples of pure waste (greatest opportunity for improvement) are associated with the idle time within a process
Pure waste activities represent the top priority for elimination
Video

## Slide 10: Single Minute Exchange of Die (SMED)
Tool/die changeovers disrupt production – production is stopped while tools/dies are changed
Idea behind SMED (originated at Toyota around 1970 by Shigeo Shingo) is that a significant portion of the die-changing operation can be done off-line while the previous die is still in place and the line continues to operate
Die-changing operation is divided into two components: inside exchange of die (IED) and outside exchange of die (OED)
OED portion is performed while the line is operating in advance of the actual exchange – the goal is to structure die change so that there are as many steps as possible in the OED portion
Tool/die changeovers typically reduced from hours to minutes

## Slide 11: Five S (5S) Methodology
5S transforms and maintains a work environment that supports lean implementation

## Slide 12: Additional Benefits of 5S Methodology
5S provides the foundation for creating discipline in the workplace
It helps cultivate relationships in the company and raises employee morale
Work areas that are neat and clean will gain credibility with customers, suppliers, and visitors to the company

## Slide 13: Value Stream
The value stream represents the linkage of all value-added and non-value-added activities associated with the creation of a product or service desired by a customer
  In manufacturing: raw materials → finished product
  In product development: design concerns → technical data package (drawings)
The goal in reviewing/studying the value stream is to maximize customer value

## Slide 14: Value Stream Map

## Slide 15: Benefits of Developing a Value Stream Map
Allows more than just the visualization of the activities in the process
Helps identify the sources of waste and impediments to flow
Helps identify the information flows as well as the product and material flows in a process
Helps reduce “cherry picking” of improvement projects

## Slide 16: Five Lean Principles
(1) Specify value in the eyes of the customer
(2) Identify the value stream and eliminate the waste
(3) Make value flow at the pull of the customer
(4) Involve and empower employees (there is no better source of insight than the employees who are performing the work)
(5) Continuously improve (kaizen) in pursuit of perfection

## Slide 17: References (sources of graphics)
Fiore, Clifford, Accelerated Product Development: Combining Lean and Six Sigma for Peak Performance, Productivity Press, NY, NY, 2005.
Hamilton, Bruce, “Toast Kaizen, An Introduction to Continuous Improvement & Lean Principles,” Greater Boston Manufacturing Partnership, University of Massachusetts, Boston, MA, 2005 (DVD).
Insights On Implementation-Improved Flow: Collected Practices and Cases, Ralph Bernstein, Editor, Productivity Press, 2006.
Jacobs, Robert F. and Chase, Richard B., Operations and Supply Management: The Core, McGraw-Hill/Irwin, NY, NY, 2008.
Nahmias, Steven, Production & Operations Analysis, 5th Edition, McGraw-Hill/Irwin, NY, NY, 2005.